CANopen specification for Panther RX

Table of content

1.	Revision history	1

2.	Introduction	2

3.	General	2

4.	Bus termination	2

5.	Selection of CANopen node ID	2

6.	Selection of CANopen baud rate	2

7.	LED indications	3

8.	Internal states	3

9.	Pre-defined connection set	4

10.	Transmit Process Data Objects (TPDO) overview	4

11.	Receive Process Data Objects (RPDO) overview	5

12.	Manufacturer Specific Objects	5

13.	Emergency Object (EMCY)	8

14.	Object Dictionary	9

# Revision history

| Version | Changes | Changed by | Date |
| --- | --- | --- | --- |
| V01 | Document created | Aron Kerekes | 2014-09-23 |
| V02 | Added complete object dictionary info | Aron Kerekes | 2014-09-24 |
| V03 | Added information on object 2002h:04h (directions) | Aron Kerekes | 2014-09-25 |

# Introduction

This document describes the CANopen specification for system Panther.

# General

The Panther receiver CANopen interface operates according to CANopen Application Layer and Communication Profile and Pre-Defined Connection Set defined in CiA DS-301 version 4.2.0.

General features:

- CANopen Slave device

- 4 freely mappable Transmit Process Data Objects (TPDO)

- 4 freely mappable Receive Process Data Objects (RPDO)

- 1 Service Data Object (SDO)

- Synchronisation Object (SYNC) Consumer

- Emergency Object (EMCY) Producer

- NMT protocols

- Bootup Protocol

- Node Guarding Protocol

- Heartbeat Protocol

- Layer Setting Service (LSS)

- CANopen Node ID selectable via User Interface: 1-127

- CANopen baudrate selectable via User Interface: 10 kbps, 20 kbps, 50 kbps, 100 kbps, 125 kbps, 250 kbps, 500 kbps, 800 kbps 1 Mbps

- Vendor ID: 0x000000A6

# Bus termination

The CANopen interface does not contain an internal bus termination resistor. If the Panther receiver is the last unit on the bus, the bus has to be terminated externally.

# Selection of CANopen node ID

The CANopen node ID is selected using the PC program Settings Manager IV. The selected node ID has to be in the range 1 to 127.

# Selection of CANopen baud rate

The CANopen baud rate is selected using the PC program Settings Manager IV. The following baud rates can be selected: 10 kbps, 20 kbps, 50 kbps, 100 kbps, 125 kbps, 250 kbps, 500 kbps, 800 kbps, 1 Mbps.

# LED indications

The CANopen interface has two indication LEDs, see table below.

Run-LED:

| LED State | Indication | Description |
| --- | --- | --- |
| Off | - | No power |
| Green | OPERATIONAL | State=OPERATIONAL |
| Green, blinking | PRE-OPERATIONAL | State=PRE-OPERATIONAL |
| Green, single flash | STOPPED | State=STOPPED |

Err-LED:

| LED State | Indication | Description |
| --- | --- | --- |
| Off | - | No power / Device is in working condition |
| Red, single flash | Warning limit reached | A bus error counter reached or exceeded its warning level. |
| Red, flickering | LSS | LSS services in progress |
| Red | Bus off (Fatal Event) | Bus off. |

# Internal states

The CANopen interface supports the following states:

| State Transition | Trigger for State Transition |
| --- | --- |
| (1) | At Power On the Initialization state is entered autonomously |
| (2) | Initialization finished – enter state PRE-OPERATIONAL automatically |
| (3), (6) | Start Remote Node indication (NMT message) |
| (4), (7) | Enter PRE-OPERATIONAL State indication (NMT message) |
| (5), (8) | Stop Remote Node indication (NMT message) |
| (9), (10), (11) | Reset Node indication (NMT message) |
| (12), (13), (14) | Reset Communication indication (NMT message) |

# Pre-defined connection set

The communication objects according to the pre-defined connection set have the following COB-IDs and communication parameters:

| Object | Default COB-ID | Communication/Mapping Parameters at Index |
| --- | --- | --- |
| NMT | 0h | - |
| SYNC | 80h | 1005h, 1006h, 1007h |
| EMERGENCY (EMCY) | 80h + Node ID | 1014h, 1015h |
| RPDO 1 | 200h + Node ID | 1400h, 1600h |
| RPDO 2 | 300h + Node ID | 1401h, 1601h |
| RPDO 3 | 400h + Node ID | 1402h, 1602h |
| RPDO 4 | 500h + Node ID | 1403h, 1603h |
| TPDO 1 | 180h + Node ID | 1800h, 1A00h |
| TPDO 2 | 280h + Node ID | 1801h, 1A01h |
| TPDO 3 | 380h + Node ID | 1802h, 1A02h |
| TPDO 4 | 480h + Node ID | 1803h, 1A03h |
| Default SDO Client->Server (rx) | 600h + Node ID | 1200h |
| Default SDO Server->Client (tx) | 580h + Node ID | 1200h |
| NMT Error Control | 700h + Node ID | 1016h, 1017h |

Default PDO transmission type is 254 (transmission when data changes).

# Transmit Process Data Objects (TPDO) overview

The default mappings of the TPDOs are listed below. These are sent from Panther receiver to the CANopen network. The index/subindex in the object dictionary is shown below each description.

TPDO 1: System status

| UNSIGNED8 | UNSIGNED8 | UNSIGNED8 | UNSIGNED8 | UNSIGNED8 | UNSIGNED8 | UNSIGNED8 | UNSIGNED8 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 | Byte 8 |
| RX packet counter / 8 | RX RSSI 4-bit | RX status 1 | RX status 2 | Active radio channel | TX Status | Load selection | Status Code |
| 2001h/01h | 2001h/05h | 2001h/03h | 2001h/04h | 2001h/08h | 2001h/09h | 2001h/0Bh | 2001h/0Ch |

TPDO 2: Buttons and directions

| UNSIGNED16 | UNSIGNED16 | UNSIGNED16 | UNSIGNED16 |
| --- | --- | --- | --- |
| Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 | Byte 8 |
| Buttons step 1 | Buttons step 2 | Buttons both steps | Directions |
| 2002h/01h | 2002h/02h | 2002h/03h | 2002h/04h |

TPDO 3: Current TX ID and slot

| UNSIGNED32 | UNSIGNED8 | Data type: N/A |
| --- | --- | --- |
| Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 | Byte 8 |
| Current TX ID | Current TX slot | Reserved | Reserved | Reserved |
| 2003h/01h | 2001h/0Ah | Not mapped |

TPDO 4: Reserved

| Data type: N/A |
| --- |
| Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 | Byte 8 |
| Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved |
| Not mapped |

# Receive Process Data Objects (RPDO) overview

The default mappings of the RPDOs are listed below. These are received by the Panther receiver from the CANopen network. The index/subindex in the object dictionary is shown below each description.

RPDO 1: System commands

| UNSIGNED32 | Data type: N/A |
| --- | --- |
| Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 | Byte 8 |
| System command | Reserved | Reserved | Reserved | Reserved |
| 2101h/01h | Not mapped |

RPDO 2: Reserved

| Data type: N/A |
| --- |
| Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 | Byte 8 |
| Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved |
| Not mapped |

RPDO 3: Reserved

| Data type: N/A |
| --- |
| Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 | Byte 8 |
| Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved |
| Not mapped |

RPDO 4: Reserved

| Data type: N/A |
| --- |
| Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 | Byte 8 |
| Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved | Reserved |
| Not mapped |

# Manufacturer Specific Objects

The following Manufacturer Specific Objects are available in the object dictionary:

| Index | Object Name | Description | Data Type | Access |
| --- | --- | --- | --- | --- |
| 2001h | Panther receiver to CANopen: System status | Packet counter, RSSI, RX/TX status, radio channel, load selection | U8 Array | RO |
| 2002h | Panther receiver to CANopen: Buttons and directions | Buttons step 1/step 2/both, directions | U16 Array | RO |
| 2003h | Panther receiver to CANopen: Current TX ID | ID of current TX if radio link is active | U32 Array | RO |
| 2101h | CANopen to Panther receiver: System Commands | System commands from CANopen | U32 Array | RW |

Object 2001h: System status

| Index: 2001h Name: System status Sub-indexes: 0Ch Data type: UNSIGNED8 Access: RO |
| --- |
| Sub-index | Description |
| 1 | RX packet counter / 8 Packet counter for the number of received radio packets by the receiver unit. It increases value by 1 for every 8th received radio packet and counts from 0 to 255, and then resets and start over again. |
| 2 | RX packet counter direct Packet counter for the number of received radio packets by the receiver unit. It increases value by 1 for every received radio packet and counts from 0 to 255, and then resets and start over again. |
| 3 | RX status 1 Bit 0: Radio link active Bit 1: Delayed radio link Bit 2: Raw radio link Bit 3: Zero position Bit 4: Start phase Bit 5: Kill function Bit 6: RSSI too strong Bit 7: RSSI too weak |
| 4 | RX status 2 Bit 0: Got stop command Bit 1: Button timeout Bit 2: Register mode active Bit 3: Extended register mode active Bit 4-7: Reserved |
| 5 | RX RSSI 4-bit Bit 0-3: Receiver RSSI level: 0000=RSSI low, 1111=RSSI high Bit 4-7: Reserved |
| 6 | RX RSSI 8-bit filtered Low-pass filtered receiver RSSI value in –dBm. |
| 7 | RX RSSI 8-bit unfiltered Unfiltered receiver RSSI value in –dBm. |
| 8 | Active radio channel 2.4GHz frequency band: Value 11-26 => radio channel 11-26 If the radio link is down and the receiver frequency scanning is active, the value for active radio channel is 00h. |
| 9 | TX status Bit 0: TX battery bad Bit 1-7: Reserved |
| 10 | TX slot Slot of currently active TX if radio link is up. If the radio link is down, this contains the value FFh. |
| 11 | Load select Bit 0-3: Load select bits A-D from TX Bit 4-7: Reserved |
| 12 | Status code Latest error code from radio packet handler. One of the following: 00h: Normal operation, no error 03h: Valid register packet received 66h: Unregistered TX 67h: Packet not accepted in register mode 68h: Bad config ID 69h: Repeated packet sequence number 6Ah: Mismatch of continuous/discontinuous mode 6Bh: Custom ID not allowed 6Ch: Login failed 6Dh: RSSI too low, packet thrown away 6Eh: Locked on other TX/Bad load selection bits |

Object 2002h: Buttons and directions

| Index: 2003h Name: Buttons and directions Sub-indexes: 04h Data type: UNSIGNED16 Access: RO |
| --- |
| Sub-index | Description |
| 1 | Buttons step 1 Bit 0 – 15: Buttons 1 – 16 step 1 |
| 2 | Buttons step 2 Bit 0 – 15: Buttons 1 – 16 step 2 |
| 3 | Buttons both steps Bit 0 – 15: Buttons 1 – 16 both steps |
| 4 | Directions Bit 00: Direction 1, position -2 Bit 01: Direction 1, position -1 Bit 02: Direction 1, position +1 Bit 03: Direction 1, position +2 Bit 04: Direction 2, position -2 Bit 05: Direction 2, position -1 Bit 06: Direction 2, position +1 Bit 07: Direction 2, position +2 Bit 08: Direction 3, position -2 Bit 09: Direction 3, position -1 Bit 10: Direction 3, position +1 Bit 11: Direction 3, position +2 Bit 12-15: Reserved |

Object 2004h: Current TX

| Index: 2004h Name: Safe state data Sub-indexes: 01h Data type: UNSIGNED32 Access: RO |
| --- |
| Sub-index | Description |
| 1 | Current TX ID ID number of currently active TX if radio link is up. If the radio link is down, this contains the value 0h. |

Object 2101h: System Commands

| Index: 2101h Name: Relay control Sub-indexes: 01h Data type: UNSIGNED32 Access: RWW |
| --- |
| Sub-index | Description |
| 1 | System command Bit 00-07: Contains the ascii value ‘T’ Bit 08-15: Contains the ascii value ‘R’ Bit 16-23: Contains the ascii value ‘C’ Bit 24-31: One of the following values: 01h: Activate register mode on RX. This will expire after a 10 sec timeout if no valid packets are received. |

# Emergency Object (EMCY)

The Emergency Object is sent to the CANopen network with the following information:

| Byte 0 | Byte 1 | Byte 2 | Byte 3 | Byte 4 | Byte 5 | Byte 6 | Byte 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| EMCY Error Code Low Byte | EMCY Error Code High Byte | Error Register (1001h) | Manufacturer specific field (not used) |

The EMCY Error Codes for internal CANopen diagnostics are interpreted as follows:

| EMCY Error Code | Description |
| --- | --- |
| 8110h | CAN controller signalled a lost message |
| 8120h | CAN controller reached the warning limit due to error frames |
| 8210h | A received PDO was smaller than specified by the valid mapping table |
| 8220h | The DLC of a received PDO exceeded the length specified by the valid mapping table |
| 8130h | An error control event has occurred (either a life guarding or a heartbeat event) |
| 8140h | CAN controller has recovered from a BUS OFF state |
| 8150h | COB-ID collision detected |

# Object Dictionary

Abbreviations:

| RO: Read Only | RW: Read, Write | U8: Unsigned8 | U16: Unsigned16 | U32: Unsigned32 |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | I8: Integer8 | I16: Integer16 | I32: Integer32 |  |  |

| General Parameters |
| --- |
| Index | Object Name | Sub-Index | Description | Data Type | Access | Note |
| 0002h | Dummy Object | 00h | Dummy Type Object for I8 | U32 | RW | 0000 0008h |
| 0003h | Dummy Object | 00h | Dummy Type Object for I16 | U32 | RW | 0000 0010h |
| 0004h | Dummy Object | 00h | Dummy Type Object for I32 | U32 | RW | 0000 0020h |
| 0005h | Dummy Object | 00h | Dummy Type Object for U8 | U32 | RW | 0000 0008h |
| 0006h | Dummy Object | 00h | Dummy Type Object for U16 | U32 | RW | 0000 0010h |
| 0007h | Dummy Object | 00h | Dummy Type Object for U32 | U32 | RW | 0000 0020h |
| 1000h | Device Type | 00h | Device Type | U32 | RO | 0000 0000h (No Profile) |
| 1001h | Error Register | 00h | Error Register | U8 | RO | - |
| 1003h | Pre-defined error field | 00h | Number of errors | U8 | RW |  |
|  |  | 01h-08h | Error field | U32 | RO |  |
| 1005h | COB-ID Sync | 00h | COB-ID Sync | U32 | RW | Default value is 0000 0080h |
| 1006h | Communication Cycle Period | 00h | Period between transmissions of SYNC in µs | U32 | RW | 0000 0000h |
| 1007h | Synchronous Window Length | 00h | Synchronous Window Length in µs (0 is disabled) | U32 | RW | 0000 0000h |
| 1008h | Manufacturer Device Name | 00h | Manufacturer Device Name | Visible string | RO | “R18-1” for Panther Fieldbus RX |
| 1009h | Manufacturer Hardware Version | 00h | Manufacturer Hardware Version | Visible string | RO | - |
| 100Ah | Manufacturer Software Version | 00h | Manufacturer Software Version | Visible string | RO | - |
| 100Ch | Guard Time | 00h | Guard Time | U16 | RW | - |
| 100Dh | Life Time Factor | 00h | Life Time Factor | U8 | RW | - |
| 1010h | Store Parameters | 00h | Largest sub-index supported | U8 | RO | 02h |
|  |  | 01h | Store all parameters | U32 | RW | Both sub-indexes have the same effect when ASCII “save” is written |
|  |  | 02h | Store Communication parameters | U32 | RW |  |
| 1011h | Restore Parameters | 00h | Largest sub-index supported | U8 | RO | 02h |
|  |  | 01h | Restore all default parameters | U32 | RW | Both sub-indexes have the same effect when ASCII “load” is written |
|  |  | 02h | Restore communication default parameters | U32 | RW |  |
| 1014h | COB-ID EMCY | 00h | COB-ID EMCY | U32 | RO | - |
| 1015h | Inhibit Time EMCY | 00h | Inhibit Time EMCY | U16 | RW | Default value is 0000h |
| 1016h | Consumer Heartbeat Time | 00h | Number of entries | U8 | RO | 01h |
|  |  | 01h | Consumer Heartbeat Time | U32 | RW | Node ID + Heartbeat Time. Value must be a multiple of 1ms. |
| 1017h | Producer Heartbeat Time | 00h | Producer Heartbeat Time | U16 | RW | - |
| 1018h | Identity object | 00h | Number of entries | U8 | RO | 04h |
|  |  | 01h | Vendor ID | U32 | RO |  |
|  |  | 02h | Product Code | U32 | RO |  |
|  |  | 03h | Revision Number | U32 | RO |  |
|  |  | 04h | Serial Number | U32 | RO |  |
| 1019h | Synchronous counter overflow value | 00h | Synchronous counter overflow value | U8 | RW | - |

| Server SDO Parameters |
| --- |
| Index | Object Name | Sub-Index | Description | Data Type | Access | Note |
| 1200h | Server SDO Parameter | 00h | Largest sub-index supported | U8 | RO | 02h |
|  |  | 01h | COB ID Client to Server (Receive SDO) | U32 | RO | Node ID + 0600h |
|  |  | 02h | COB ID Server to Client (Transmit SDO) | U32 | RO | Node ID + 0580h |
| Receive PDO Communication Parameters |
| Index | Object Name | Sub-Index | Description | Data Type | Access | Note |
| 1400h … 1403h | Receive PDO Communication Parameter | 00h | Largest sub-index supported | U8 | RO | 02h |
|  |  | 01h | COB-ID used by PDO | U32 | RW | - |
|  |  | 02h | Transmission Type | U8 | RW | - |
| Receive PDO Mapping Parameters |
| Index | Object Name | Sub-Index | Description | Data Type | Access | Note |
| 1600h … 1603h | Receive PDO Mapping Parameter | 00h | Number of mapped application objects in PDO | U8 | RW | 00h – 08h |
|  |  | 01h | Mapped object No.1 | U32 | RW | - |
|  |  | 02h | Mapped object No.2 | U32 | RW | - |
|  |  | … | … | U32 | RW | - |
|  |  | 08h | Mapped object No.8 | U32 | RW | - |
| Transmit PDO Communication Parameters |
| Index | Object Name | Sub-Index | Description | Data Type | Access | Note |
| 1800h … 1803h | Transmit PDO Communication Parameter | 00h | Largest sub-index supported | U8 | RO | 05h |
|  |  | 01h | COB-ID used by PDO | U32 | RW | - |
|  |  | 02h | Transmission Type | U8 | RW | - |
|  |  | 03h | Inhibit Time | U16 | RW | - |
|  |  | 05h | Event Timer (ms) | U16 | RW | - |
| Transmit PDO Mapping Parameters |
| Index | Object Name | Sub-Index | Description | Data Type | Access | Note |
| 1A00h … 1A03h | Transmit PDO Mapping Parameter | 00h | Number of mapped application objects in PDO | U8 | RW | 00h – 08h |
|  |  | 01h | Mapped object No.1 | U32 | RW | - |
|  |  | 02h | Mapped object No.2 | U32 | RW | - |
|  |  | … | … | U32 | RW | - |
|  |  | 08h | Mapped object No.8 | U32 | RW | - |

| Manufacturer Specific Parameters, outgoing |
| --- |
| Index | Object Name | Sub-Index | Description | Data Type | Access | Note |
| 2001h | Panther Receiver to CANopen: System status | 00h | Largest sub-index supported | U8 | RO | 0Ch |
|  |  | 01h | RX packet counter / 8 | U8 | RO | - |
|  |  | 02h | RX packet counter direct | U8 | RO | - |
|  |  | 03h | RX status 1 | U8 | RO | - |
|  |  | 04h | RX status 2 | U8 | RO | - |
|  |  | 05h | RX RSSI 4-bit | U8 | RO | - |
|  |  | 06h | RX RSSI 8-bit filtered | U8 | RO | - |
|  |  | 07h | RX RSSI 8-bit unfiltered | U8 | RO | - |
|  |  | 08h | Active radio channel | U8 | RO | - |
|  |  | 09h | TX status | U8 | RO | - |
|  |  | 0Ah | TX slot | U8 | RO | - |
|  |  | 0Bh | Load select | U8 | RO | - |
|  |  | 0Ch | Status code | U8 | RO | - |
| 2002h | Panther Receiver to CANopen: TX buttons and directions | 00h | Largest sub-index supported | U8 | RO | 0Ah |
|  |  | 01h | Buttons step 1 | U16 | RO | - |
|  |  | 02h | Buttons step 2 | U16 | RO | - |
|  |  | 03h | Buttons both steps | U16 | RO | - |
|  |  | 04h | Directions | U16 | RO | - |
| 2003h | Panther Receiver to CANopen: Current TX | 00h | Largest sub-index supported | U8 | RO | 04h |
|  |  | 01h | Current TX ID | U32 | RO | - |

| Manufacturer Specific Parameters, incoming |
| --- |
| 2101h | CANopen to Panther Receiver: System commands | 00h | Largest sub-index supported | U8 | RO | 01h |
|  |  | 01h | System command | U32 | RWW | - |

# Text boxes

(14)

(13)

(12)

(9)

(10)

(11)

(8)

(7)

(6)

(5)

(4)

(3)

(2)

(1)

Initialization

Pre-Operational

Operational

Stopped

Power On